## Slide 1: Streams Across Landscapes (SAL)
Jim Graham, PhD
Humboldt State University
Arcata, California, USA
JULIA Petreshen
Thomas Gast & Associates Environnemental Consultants
Arcata, California, USA
A new method for modeling stream flow in small watersheds

## Slide 2: Why We Created SAL
The amount of water, and it’s characteristics, are key to determining emigration, spawning, rearing, and out migration potential for salmonids.
Modeling allows us to recreate historic stream flow and for scenarios in the future
Existing stream flow modeling approaches require calibration to a stream flow gauge
  Not always available
  Shifts model off reality unless diversions are accounted for
Need a modeling approach that:
  Does not require calibration to a stream gauge hydrograph
  Allows for accounting for diversions and lakes

## Slide 3: Elder Creek Watershed
Confluence with Southern Fork of the Eel River
Gauge Station
Confluence with Tributary

## Slide 5: Approach
Created within BlueSpray
  GIS application originally from SchoonerTurtles, Inc.
  Combines open source libraries with custom code to create a flexible development environment
Java based application
  Runs on MS-Windows, UNIX, Linux, Mac
Standard file formats for inputs and outputs
  TIFF, Shapefiles, CSVs, etc.
Creates web pages to visualize results

## Slide 7: Data
Digital Elevation Model (DEM)
  30 meters works well
  All cells within the watershed, except lakes, flow to the pour point
Pour Point for Watershed
Weather Data
  Precipitation
  Required for ET: Wind, Temp, Humidity
    Solar Radiation: provided or automatic
Stream Gauge Data (optional)
Cover type (optional)
  Types provided for National Land Cover Data (NLCD)
Soil Data (optional)
  BlueSpray includes features to create soil layers from SSURGO polygons

## Slide 8: Flexibility
Any spatial resolution:
  30 meters seems to work well
Weather and discharge data at 5 minutes to daily
Time cycles from 5 minutes to daily
Any number & depth of soil layers:
  4-6 layers for first 2 meters
Cover type and age (converted to height)
Soil type and rock proportion at various depths

## Slide 9: Elder Creek Model
Complete weather data at 15 minute intervals
  Precip, Temp, Wind Speed, Humidity, Solar Radiation
USGS stream gauge at 10 minute intervals resampled to 15 minute
Cover type from NLCD
Age from LEMMA
Cover Type from NLCD
Cover Age from LEMMA
Soil Data from SSURGO: Type and Proportion Rock

## Slide 10: NLCD Cover Type Data
Elder Creek is almost all evergreen forest

## Slide 11: SSURGO Soil Type Data
Each soil type has different properties for moving water
First soil layer is dominated by plant material

## Slide 12: Proportion Rock
Flow is restricted by rock
Notes: Run video example

## Slide 13: Results
Best Nash–Sutcliffe Model Efficiency Coefficient:
  0.8764
  For 2015 through 2017

## Slide 14: Additional features
Diversions
  Move water from streams to surface, etc.
Modifications
  Change rasters at points in time
  Simulate harvests, plantings
Lakes
  Simulate storage and evaporation

## Slide 15: Next Steps
Data:
  Developing cover type and age based on LiDAR and NAIP data for entire Eel River watershed
  Validation against a system that is dryer than Elder Creek
Additional Features:
  Macropores
  Springs (upwelling)
  Snow?
  Fog absorption?
  Ground water level?
Testing, documentation improvements, etc.

## Slide 16: Acknowledgements
Thanks to:
  VELMA team at the EPA
  Dr. Lawrence Dingman for the textbook Physical Hydrology
  Angelo Coast Range Reserve:
    University of California Natural Reserve System
Example Outputs:
  http://gsp.humboldt.edu/websites/watersheds/ElderCreek/
Questions?
  James.graham@humboldt.edu